1. Freeze a baseline configuration
Pick one initial design point and stop moving the big parameters every day.
Freeze, at least for Baseline A:
MTOW target
preferred design mass: 13.5–14.5 kg
absolute upper limit: 15.0 kg
payload = 3.0 kg
wing area, span, and rough planform
wing area = 0.90 m²
wingspan = 2.70 m
aspect ratio ≈ 8.1
planform = straight, mildly tapered wing
taper ratio = about 0.65 to 0.75
sweep = zero or very small
dihedral = small, around 2–3° if desired
root chord ≈ 0.40 m
tip chord ≈ 0.27 m
MAC roughly in the low 0.33 m range
fuselage length
fuselage length = 2.20 m
rotor diameter
rotor diameter = 22 in - absolute maximum it could go
All 4 rotors would have the same diameter
rotor positions
4 tilt rotors total
2 wing-mounted
2 aft-mounted, integrated with the V-tail support structure
all four hubs symmetric about centerline
CG must remain inside rotor footprint in top view
Front rotors
- x = 0.95 m from nose
- y = ±0.80 m from centerline
Rear rotors
- x = 1.85 m from nose
- y = ±0.55 m from centerline
These are not final CAD coordinates, but they are a very good frozen starting layout.
V-tail size and arm
V-tail arm = 0.95 m
measured approximately from wing aerodynamic center to V-tail aerodynamic center
- total V-tail projected area = 0.22 to 0.26 m²
- use 0.24 m² baseline
- two identical tail surfaces
- tail angle 45° to horizontal as a first assumption
- moderate taper
- simple straight leading/trailing edges
A practical starting point per surface could be roughly:
- surface span along panel ≈ 0.55–0.65 m
- mean chord ≈ 0.18–0.22 m
battery target mass/energy
battery mass = 3.0 kg baseline
installed battery energy = 500 Wh baseline
- payload placeholder mass
- target CG range
target nominal CG = 28% MAC
forward CG limit = 24% MAC
aft CG limit = 32% MAC

2. Make the first real 3-view layout
Now produce a proper top, side, and front view with dimensions.
It should show:
- wing
- fuselage
- V-tail
- four rotor hubs
- full prop disks
- landing gear
- battery volume
- payload volume
- avionics volume
- estimated CG and CG range
This step is where you verify:
- rear rotors clear the V-tail in all tilt positions
- front rotors clear the wing and fuselage
- CG lies inside the rotor footprint
- landing stance is stable
- boom and nacelle geometry are realistic
For your concept, this is one of the most important next steps.

3. Build a real mass and CG model
Your sizing loop used approximate grouped masses. Now turn that into a component-level model.
Make a table with:
- each component name
- mass
- x, y, z position
- moment contributions
Include:
- wing structure
- fuselage structure
- V-tail structure
- front motors
- rear motors
- front nacelles
- rear nacelles
- tilt actuators
- ESCs
- battery
- payload
- autopilot
- GPS
- telemetry
- wiring
- power distribution
- landing gear
- fasteners/brackets
Then calculate:
- total mass
- CG location
- forward and aft CG cases
You want to know early whether the aircraft can still balance once real components are placed.

4. Define the control concept clearly
Before detailed CAD, you need to know how the aircraft will actually be controlled.
Define for:
Hover
- roll control
- pitch control
- yaw control
Forward flight
- roll control
- pitch control
- yaw control
Transition
- when tilt begins
- how tilt is scheduled
- how rotor thrust and control surfaces blend
- what happens if one axis becomes weak during transition
For your aircraft, this is especially important because:
- you have a wing pair and a tail pair of rotors
- you have a V-tail instead of a conventional tail
- the rear tilt rotors and tail surfaces interact strongly
You do not need the full final control law yet, but you do need a clear control allocation concept.

5. Choose the avionics and autopilot stack
You should decide the prototype flight-control architecture now.
That means choosing:
- autopilot hardware
- IMU / GPS / compass arrangement
- RC link
- telemetry link
- power monitoring
- logging
- airspeed sensing if used
- tilt-servo control integration
- redundancy level for the prototype
A prototype is much easier to develop when the avionics architecture is fixed early.

6. Design the propulsion system properly
Now move from generic thrust numbers to actual candidate hardware.
Select candidate:
- motors
- propellers
- ESCs
- battery voltage
- current limits
- connectors
- wiring gauge
- power distribution method
Check:
- thrust per rotor
- current per motor
- thermal margins
- hover throttle point
- cruise throttle point
- efficiency region
- expected peak power during transition
You want enough thrust margin that the aircraft is not hovering near full throttle.

7. Design and de-risk the tilt mechanism
This is a major subsystem for your aircraft.
Before full-aircraft build, define:
- pivot location
- bearing arrangement
- actuator type
- actuator torque requirement
- hard stops
- position sensing
- wiring routing through moving parts
- backlash limits
- locking or holding method if needed
Then build at least one representative tilt-mechanism test article.
Test:
- stiffness
- repeatability
- backlash
- actuator speed
- heating
- vibration
- mechanical durability
For your concept, this is one of the smartest things you can do before cutting the full airframe.

8. Define the structural concept before detailed CAD
Now decide what carries the loads.
You should be able to point to:
- main wing spar
- fuselage keel or tube frame
- nacelle supports
- rear boom/tail support structure
- landing gear load paths
- V-tail attachment structure
Then ask:
- how do front rotor loads enter the wing?
- how do rear rotor loads enter the tail boom or aft structure?
- how are hover loads carried?
- how are forward-flight bending and torsion carried?
- where are the high-risk joints?
The rear nacelles are probably one of the most structurally critical parts of your design.

9. Create an initial CAD package
Once the layout, CG, propulsion, and structural concept are believable, start the first CAD embodiment.
Model:
- fuselage shell or frame
- wing
- V-tail
- booms
- nacelles
- tilt joints
- landing gear
- internal battery and payload bays
At this stage, CAD is mainly for:
- packaging
- interference checking
- mount design
- manufacturing planning
Not for over-polishing the shape.

10. Run the first engineering checks
Before fabrication, do a first pass of sanity checks:
Aerodynamic / configuration checks
- CG vs wing MAC
- tail arm and tail effectiveness
- control surface sizing
- prop/airframe interference
Structural checks
- wing bending estimate
- boom bending estimate
- nacelle mount loads
- landing impact loads
- tail attachment loads
Power checks
- hover power margin
- ESC current margin
- battery C-rate
- cable heating
These can be approximate first-order checks. They do not need to be perfect yet.

11. Plan the prototype around adjustability
Your first prototype should be easy to tune, not locked down.
Build in adjustment for:
- battery position
- CG trimming
- nacelle angle calibration
- tail incidence shims if possible
- control surface neutral settings
- removable nacelles
- easy access to avionics and power system
This will make the flight-test phase far easier.

12. Make a ground and bench test plan before manufacturing is complete
Do not wait until the aircraft is built to think about testing.
Create a test ladder:
Bench tests
- motor/prop thrust tests
- ESC and current tests
- battery endurance checks
- tilt actuator tests
- servo/control-surface checks
- telemetry/logging validation
Structural ground tests
- wing static load check
- nacelle stiffness check
- landing gear drop/static check
- tail stiffness check
Integrated system tests
- powered tilt tests
- vibration tests
- restrained thrust tests
- control-direction checks
- failsafe tests
Flight expansion
- restrained hover
- low-altitude hover
- hover translation
- partial tilt
- partial transition
- full forward flight
- full transition
That plan should exist before the airplane is finished.

13. Define safety and failure strategy
For an experimental prototype, decide now:
- kill switch logic
- lost-link behavior
- low-voltage behavior
- tilt actuator failure behavior
- motor failure response philosophy
- preflight checklist
- arming procedure
- test area requirements
This is not paperwork for later. It is part of the design.

14. Manufacture a subscale or subsystem article if needed
If any area still feels high-risk, test it separately first.
For your aircraft, the best subsystem candidates are:
- rear tilt nacelle + V-tail interference mockup
- one full tilt mechanism assembly
- one wing/nacelle structural bay
- propulsion bench test stand
A small investment here can prevent a full-airframe redesign later.

15. Then build Prototype A for learning, not perfection
Your first 15 kg aircraft should be optimized for:
- robustness
- access
- repairability
- data collection
- conservative flying qualities
Not for:
- minimum drag
- perfect finish
- maximum payload
- production aesthetics
A successful prototype is one that teaches you and survives enough tests.